## Slide 1: ALARM CLOCK USING ARDUINO
PC-108 ICT FOR FRESHERS
Submitted to :- Prof. Anil Roy
Submitted by :- Raman kumar (201301202)

## Slide 2: PROJECT INTRODUCTION:
In this project, we made a alarm clock using rtc DS-3231. This module is very cheap. In this we used Arduino.
Time is getting by RTC DS-3231.
Buzzer is beeped after comparing the current time with alarm time.

## Slide 3: COMPONENTS REQUIRED :
Arduino
16x2 LCD
DS-3231
Buzzer
10k potentiometer
10 ohm resistor
Connecting wires
Breadboard

## Slide 4: DS3231 REAL TIME CLOCK MODULE:
The DS3231 is a low cost RTC which maintains hours, minutes and seconds as well as dates.
This module can works on 5v.
VCC and GND pins are for powering the module.
Two pins SDA(data line) and SCL(clock line) pins.
SDA pin is connected to A4 pin of arduino and SCL pin is connected to A5 pin of arduino.

## Slide 5: CONNECTIONS OF LCD TO ARDUINO :
Pin 1 on the LCD to ground.
Pin 2 on the LCD to 5V.
Pin 3 on the LCD to the middle pin on the 10K potentiometer.
Pin 4 on the LCD to digital pin 2 on the Arduino.
Pin 5 on the LCD to the ground of Arduino.
Pin 6 on the LCD to the pin 3 of Arduino.
Connect the data pins (D4-D7) to the pins 4, 5, 6, 7 on the Arduino.
Pin 15 to the 5V pin on the Arduino through the 10-ohm resistor.
Pin 16 to ground.

## Slide 6: CONNECTIONS OF BUZZER TO ARDUINO:
Positive pin of buzzer connected to pin 11 of arduino
And other one is connected to GND of arduino.

## Slide 7: HOW DOES IT WORK :
We get the time and date from the RTC module using library functions. And that time will be compared with alarm time, which we have set in code.
If the current time is matched with alarm time then buzzer will beep. The beeping time, we can set in code. We have put 2 minute in this code. We can increase beeping time after changing in code.
The time and date will display on LCD.

## Slide 8
THANK YOU